## Slide 1: Spatiotemporal Analysis of PM2.5 and Meteorological Parameters (2021–2024)
Ground Data Cleaning, Station Selection, and Gap Filling (Week 1 & 2 Update)
- Archie Mittal (2024CS10560) - Yashwardhan Singh Choudhary (2024CS10300)

## Slide 2: Project Overview & Data Source
Objective: To analyze PM2.5 trends and their relationship with wind parameters across multiple stations.
Data Source: Central Pollution Control Board (CPCB) Hourly Data available of 39 stations.
Temporal Coverage: January 2021 to December 2024.
Parameters Studied: PM_2.5 (Particulate Matter)
Wind Speed (WS)
Wind Direction (WD)

## Slide 3: Task 1 – Robust Data Organization
Goal: Standardize file structures and assess raw availability.
Actions:
Developed a "Robust Mapping" script to identify target columns using keyword matching (Regex).
Organized raw files into a structured hierarchy based on site_id and year.
Key Deliverable: station_availability_summary_robust.csv.
This file tracked the percentage of non-null data for every station-year combination.

## Slide 4: Task 2 – Station Selection Criteria
Goal: Filter for high-quality, continuous data.
The 70% Rule: A station was only selected if PM_2.5, Wind Speed, and Wind Direction all had > 70% availability for every single year from 2021 to 2024.
Results:
Original: 39 stations.
Selected: 26 stations met the rigorous quality threshold.
Deliverable: final_selected_stations.csv.

## Slide 5: Task 3 – Column Standardization
Process: To ensure seamless analysis across 26 folders, all CSVs were reformatted.
Mapping: timestamp ->Standard Datetime format.
PM 2.5 ->Standardized unit/name.
wind_speed & wind_dir ->Unified labels.
Result: A clean, analysis-ready directory: final_station_data_clean/ which contains all the 26 stations and each of them contains separate datasets for the respective years i.e. 2021 to 2024.

## Slide 6: Task 4 – Temporal Gap Filling
Problem: Even high-quality stations have "micro-gaps" (1–3 missing hours) which disrupt time-series modeling.
Strategy: Linear Interpolation.
Threshold: Only gaps <= 3 hours were filled.
Why? To maintain scientific integrity. Large gaps (e.g., 24 hours) cannot be accurately estimated by simple means.
Outcome: Improved data continuity for diurnal cycle analysis.
Deliverable: final_availability_after_fill.csv

## Slide 7: Comparison Analysis (Before vs. After)
Impact: Average PM_2.5 availability: Increased by approximately 1.49%.
Wind Speed Availability: Increased by approximately 0.76%.
Visual Proof:

## Slide 8: Conclusion & Next Steps
Summary: We have established a high-quality dataset of 26 stations with standardized metrics and filled temporal gaps.
Future Work: Seasonal Trends & Station Correlations
Seasonal Profiles: Identify PM_2.5 peaks across Winter, Monsoon, and Post-Monsoon periods (2021–2024).
Spatial Heatmaps: Create a correlation matrix to identify which stations share similar pollution patterns.

## Slide 9: Week 3: Seasonal and Monthly Analysis of PM₂.₅ (2021–2024)
Objective: Analyze seasonal and monthly variability of PM₂.₅ across selected CPCB stations.
Dataset: 26 stations with hourly PM₂.₅ data (2021–2024).
Focus: Seasonal trends, monthly evolution, and meteorological interpretation.
Diurnal Variations & Behavioral Analysis
Objective: To characterize the "Heartbeat" of Delhi’s air pollution by analyzing hourly PM_2.5 fluctuations across 26 stations over a 4-year period (2021–2024).
Core Question: How do human activity (emissions) and atmospheric physics (meteorology) interact to create daily pollution cycles?
Deliverables:
Processed Dataset: diurnal_pm2.5_seasonwise.csv (Aggregated network-wide hourly averages).
Primary Visualization: diurnal_trends_comparison.png (Comparative seasonal 24-hour profiles).

## Slide 10: Seasonal Classification Methodology
We added a season column by mapping calendar months to standard Indian climatological seasons.
Seasonal bins used:
Winter: December–February
Pre-monsoon: March–May
Monsoon: June–September
Post-monsoon: October–November
The cleaned datasets were overwritten to ensure consistent seasonal labeling for all downstream analyses

## Slide 11: PM₂.₅ Aggregation Strategy
Seasonal PM₂.₅ statistics were computed independently at each station for each year.
Station-level seasonal means were first averaged across years (2021–2024).
Network-level seasonal PM₂.₅ was then obtained by equally weighting all stations.
This approach prevents dominance by any single station or year.

## Slide 12: Seasonal Average PM₂.₅ (Network Mean)
Winter and post-monsoon seasons exhibit the highest PM₂.₅ concentrations.
Monsoon shows the lowest PM₂.₅ levels due to wet scavenging and enhanced ventilation.
Pre-monsoon displays transitional PM₂.₅ behavior.
High winter PM₂.₅ is driven by shallow boundary layer heights and frequent temperature inversions.
Post-monsoon enhancement is linked to crop residue burning and reduced atmospheric dispersion.
Monsoon PM₂.₅ reduction is caused by rainfall-driven washout and stronger winds.
Pre-monsoon reflects mixed influence of dust resuspension and improved mixing.

## Slide 13: Monthly Average PM₂.₅ (Network Mean, 2021–2024)
Monthly PM₂.₅ peaks during November–January due to post-monsoon biomass burning and wintertime atmospheric stagnation.
Lowest PM₂.₅ levels occur during July–August because of intense rainfall and wet scavenging.
A sharp rise in October marks the transition from monsoon to post-monsoon pollution buildup.
Consistency across years highlights the dominant role of seasonal meteorology.

## Slide 14: Month-wise PM₂.₅ Behavior
Jan: Very high PM₂.₅ — peak winter pollution
Feb–Mar: Declining PM₂.₅ — improved ventilation
Apr–May: Moderate PM₂.₅ — dust and enhanced mixing
Jun: Drop in PM₂.₅ — onset of pre-monsoon rainfall
Jul–Aug: Lowest PM₂.₅ — monsoon washout
Sep: Slight increase — monsoon withdrawal
Oct: Sharp rise — post-monsoon onset
Nov: Maximum PM₂.₅ — stubble burning and stagnation
Dec: Very high PM₂.₅ — winter buildup

## Slide 15: Diurnal Heartbeat of Delhi’s PM₂.₅ Understanding the Daily Cycle: Rush Hours vs. Atmospheric Physics
The Double-Peak Pattern: Across all seasons, the data reveals two distinct peaks:
Morning Peak (08:00 – 10:00): Driven by the resumption of traffic (rush hour) and domestic emissions, coinciding with a still-shallow morning mixing layer.
Evening/Night Peak (20:00 – 22:00): Often higher than the morning peak. This is caused by the "collapse" of the atmospheric boundary layer after sunset, trapping emissions near the ground.
The Afternoon Dip (14:00 – 16:00): PM_2.5 levels are consistently at their lowest during the mid-afternoon.
Why? Solar heating triggers Vertical Mixing. As the ground warms, air rises, increasing the "Mixing Height" and diluting pollutants.

## Slide 16: Seasonal Variability & Boundary Layer Severity Seasonal Contrast: Why Winter and Post-Monsoon Skyrocket
Magnitude Divergence:
Winter & Post-Monsoon: Both hit massive peaks exceeding 260–280 µg/m³.
Monsoon: Shows the most stable profile (66–86 µg/m³). Rain scavenging (washout) and higher humidity prevent major accumulation.
The "Lid" Effect (Thermal Inversion):
In Winter, the nighttime cooling of the ground is so intense that it creates a "Temperature Inversion." This acts as a physical lid, trapping all pollutants within 100-200 meters of the surface, causing the extreme spikes seen in your data.
Post-Monsoon Dynamics:
Captures the unique "tail" of pollution from midnight to 4 AM (~268 µg/m³), reflecting the arrival of transported biomass smoke under stagnant night conditions.

## Slide 17: Summary of Findings Physical Interpretations & Statistical Summary
Season | Diurnal Range (Peak-Trough) | Atmospheric State
Winter | 118.4 µg/m³ | Highly Stable / Frequent Inversions
Post-Monsoon | 120.8 µg/m³ | Stagnant / Accumulation Phase
Pre-Monsoon | 92.6 µg/m³ | Turbulent / Dust-Heavy
Monsoon | 20.5 µg/m³ | Unstable / High Ventilation
Conclusion:
PM_2.5 concentration is a function of Emissions ÷ Volume. In the afternoon, the "Volume" (PBL height) is large, leading to lower concentrations. At night, the "Volume" is tiny, leading to toxic air.
Impact: This confirms that policy interventions must account for meteorology; the same emission levels produce much higher health risks at 9 PM than at 3 PM.

## Slide 18: Week 3 Conclusion & Week 4 Outlook
Seasonal Baseline: Analysis confirms Winter and Post-Monsoon pollution levels are 300% higher than Monsoon.
The ABL Driver: Diurnal trends prove PM_2.5 is controlled by the Atmospheric Boundary Layer (ABL). High nighttime levels are caused by the "Lid Effect" (Thermal Inversion) trapping pollutants.
Core Insight: Pollution peaks when emissions meet stagnant atmospheric conditions, regardless of station location.
Next Steps: Week 4 (Meteorological Conditioning)
Wind-Rose Analysis: Transitioning from When it happens to Where it comes from.
Source Tracking: Mapping PM_2.5 against wind speed and direction.
Cluster Analysis: Identifying if specific wind corridors (e.g., North-Westerly) are the primary drivers of the seasonal spikes found in Week 3.

## Slide 19: Week 4 – Meteorological Conditioning & Transport Diagnostics
• Objective: Diagnose whether extreme PM₂.₅ events are driven by:
            Ventilation suppression (low wind speeds)
            Directional transport corridors
            Or a combination of both
Methodology:
Regional segmentation (4 zones)
Percentile-based extreme filtering (Top 15%)
Wind speed comparison (Background vs Extreme)
Directional enrichment analysis (next step)

## Slide 20: Regional Classification of Stations
North → Haryana/NW transport belt(Rohini, Jahangirpuri, Ashok Vihar, Wazirpur, Narela, Bawana)
East → UP/Trans-Yamuna corridor(IHBAS (Dilshad Garden), Anand Vihar, Patparganj, Vivek Vihar, Sonia Vihar, Pusa)
South/Central → Urban accumulation core(Mandir Marg, Jawaharlal Nehru Stadium, Major Dhyan Chand National Stadium, RK Puram, Okhla Phase II, Nehru Nagar, Sri Aurobindo Marg, Dr. Karni Singh Shooting Range)
West/SW → Rajasthan boundary & industrial influence(hadipur, NSIT Dwarka, Punjabi Bagh, Dwarka Sector 8, Najafgarh, Mundka)

## Slide 21: Ventilation Suppression During Extreme Events
Wind speed decreases during extreme PM₂.₅ hours across most regions and seasons
• Strongest suppression observed in Winter (≈21–33%)
• Moderate suppression in Post-monsoon (≈16–26%)
• Weaker but consistent suppression in Pre-monsoon (≈15–23%)
• Minimal or negligible suppression during Monsoon
• Seasonal influence is stronger than regional differences

## Slide 22: Week 4 Mechanism Synthesis
• Winter: Strong ventilation suppression across all regions
• Post-Monsoon: Mixed stagnation + directional reinforcement
• Pre-Monsoon: Transitional regime (dust + moderate suppression)
• Monsoon: Weak meteorological control
Conclusion: Seasonal meteorology dominates extreme PM2.5 formation more than spatial location.

## Slide 23: PDF-based Transport Diagnostics of Extreme PM₂.₅ (DJF 2021–2024) Regional analysis for Delhi: North, East, South_Central, West_SW
Methods: KDE-based PDFs, top-15% percentile extremes, directional enrichment (extreme/background)
Objective: “Diagnose whether extreme PM₂.₅ events are driven by ventilation suppression or directional transport corridors.”
Hourly PM₂.₅ & wind (dir, speed) from cleaned station dataset (2021–2024).
Regions: North, East, South_Central, West_SW (list stations or refer to appendix).
Months: Dec–Jan–Feb (DJF), 4 years (2021–2024).
Approach:
  Build region-level hourly stacks (equal station weighting).
  Compute PM₂.₅ PDFs (KDE) for each region per year/month.
  Define extremes as top 15% PM₂.₅ hours (85th percentile).
  Directional enrichment = (freq during extreme) ÷ (background freq).

## Slide 24: Year 2021
Dec–North region has a higher probability of very high PM₂.₅ in Dec 2021 (more extreme events). Could be weaker ventilation (stagnation) or stronger source + transport into North.
Jan –West/East show concentrated moderate pollution, while North has higher probability of extremes — suggests transport from other regions combined with local stagnation.
Feb – Same pattern: North more extreme-prone; West/East more moderate but frequent pollution.

## Slide 25: Year 2022
Dec –More homogeneous pollution regimes across regions in Dec 2022 – possibly due to a region-wide meteorological pattern (e.g., synoptic stagnation or uniform emissions/transport).
Jan –January 2022 shows less stark inter-regional contrast than 2021.
Feb –Regional differences are reduced in 2022 (less directional dominance or more similar emissions).

## Slide 26: Year 2023
Dec –West_SW shows frequent moderate events; North still has moderate extremes risk.
Jan –Jan 2023 again relatively uniform; suggests common synoptic forcing.
Feb –Feb 2023: East/West often experience frequent moderate pollution but North remains more likely to experience high extremes.

## Slide 27: Year 2024
Dec –West_SW frequently experiences moderate events, South_Central sometimes slightly elevated.
Jan –Jan 2024 shows West_SW dominated by many moderate events; extremes less frequent there.
Feb –Again pattern recurs: West_SW/East often concentrated moderate events; North more tail-heavy (extreme probability).

## Slide 28: Overall takeaways
Across most years and months North frequently has a broader distribution and heavier right tail → higher probability of extreme PM₂.₅ events.
West_SW often shows sharp, high modal peaks at lower PM (frequent moderate pollution), especially in Jan/Feb (consistent across years).
East and South_Central are usually intermediate — sometimes overlapping closely depending on year/month.
When all four curves cluster closely (e.g., parts of 2022), this suggests widespread synoptic forcing rather than a single transport corridor dominating.

## Slide 29: Directional Enrichment plots (Enrichment = fraction of wind directions observed during extreme hours ÷ fraction in the background; values >1 indicate a sector is over-represented during extremes.)
EAST REGION
Interpretation: Northerly winds (N) and southerly (S) are slightly enriched during extreme PM₂.₅ events in East. So episodes there commonly occur when the wind has a northerly component and sometimes southerly inflow — mixed transport influence.

## Slide 30: NORTH REGION
Interpretation: Northerly sector is under-represented during extremes (N 0.44), while E and SE and NE are enriched (≈1.1–1.28). This implies extremes in the North region are associated with easterly/SE winds — i.e., pollution being transported into northern stations from east/southeast corridors (possibly from urban core or Trans-Yamuna influences).

## Slide 31: SOUTH_CENTRAL REGION
Interpretation: Strong enrichment from the North (1.86) — very likely that northern transport (Haryana/NW belt) strongly contributes to extremes in South_Central. Also NW is enriched. This is a clear transport-dominated signature from the north.

## Slide 32: WEST_SW REGION
Interpretation: Strong enrichment from SW, S, SE, NE (SW = 1.37 highest) — this indicates extremes at West_SW are associated with southerly–southwesterly winds (likely bringing in pollution from industrial/aggregated emission sources to the southwest/west). NW & N under-represented.

## Slide 33: OVERALL ENRICHMENT TAKEAWAYS
South_Central: most clearly dominated by northerly transport during extremes (N = 1.86).
West_SW: strongly dominated by southwest / southerly transport (SW 1.37, S 1.33).
North: extremes in this region correlate with E/SE winds (transport from east / Trans-Yamuna corridor).
East: mixed signals but N shows enrichment (N = 1.37) — Northern transport matters there, too.
These enrichment numbers directly answer the question: which direction(s) dominate extreme PM₂.₅ events at each region.

## Slide 34: Mechanistic interpretation (transport vs ventilation)
Where enrichment ratio for one or more sectors is >1.2–1.3 (e.g., South_Central N = 1.86; West_SW SW = 1.37), the extreme events are strongly associated with directional transport from those sectors — i.e., air mass advection bringing pollution to the region.
Where PDFs show heavy right tails (e.g., North in many months), this suggests either local accumulation (stagnation) or advection of already-polluted air masses; enrichment plots tell which direction these air masses come from. For instance, North’s heavy tail + enrichment for E/SE implies that extremes there are likely driven by directional inflow from the east/southeast combined with meteorological conditions that limit dispersion.
When all region PDFs overlap tightly (e.g., Dec 2022), it likely reflects synoptic-scale conditions (widespread stagnation or uniform pollution) rather than a single transport corridor.

## Slide 35
Upgraded Stagnation Index: India-ASI
Inspired by Zhou et al. (2024), Nature Communications, 15, 7448
Condition | Threshold | Physical Meaning | Source
1. Calm Wind | WS10m < 3.2 m/s | Pollution cannot disperse horizontally | NOAA ASI (Wang & Angell 1999)
2. Temperature Inversion | T925hPa - T2m > 0 K | Warm air aloft acts as a lid; pollution cannot escape vertically | India-ASI (Zhou et al. 2024)
3. No Rain | Precip < 1 mm/day | No wet scavenging (washout) of particulate matter | NOAA ASI (Wang & Angell 1999)
A day is classified as stagnant ONLY when ALL THREE conditions are met simultaneously.
Key improvement over old method: The NOAA index uses 500 hPa wind speed for vertical dispersion, but Zhou et al. showed this is poorly correlated with PM₂.₅ over India (R = −0.14). The T925–T2m inversion criterion correlates much better (R ≥ 0.63).
Data: ERA5 reanalysis (0.25°), 2×2 grid cells over Delhi, 2021–2024

## Slide 36
India-ASI: Condition Breakdown & Climatology
Month | Calm Wind (ws10m<3.2) | Inversion (T925>T2m) | Dry Day (precip<1mm) | ALL 3 Met (Stagnant)
October | 97.0% | 4.8% | 75.8% | 3.8%
November | 99.0% | 30.0% | 86.2% | 27.7%
December | 90.9% | 58.3% | 79.2% | 47.8%
January | 87.7% | 41.7% | 54.8% | 27.4%
February | 86.1% | 33.2% | 72.8% | 26.5%
Climatology: Mean India-ASI Stagnant Days per Month (2021–2024 average)
Month | Oct | Nov | Dec | Jan | Feb
Domain Avg (days) | 1.19 | 8.31 | 14.81 | 8.50 | 7.50
Key Insights:
October: Nearly zero stagnation — inversions occur only 4.8% of days. Surface is still warm, no lid forms.
December: Peak stagnation (47.8%) — strong inversions (58.3%) + dry conditions (79.2%). Half the month is truly trapped.
January: Drops below December due to Western Disturbance activity bringing rain (only 54.8% dry days).

## Slide 37
India-ASI Stagnation Anomaly — October
October marks the post-monsoon transition. Inversions are rare (4.8%), so India-ASI stagnation is near zero. Anomalies are small (±1–2 days). Oct 2021 shows a mild negative (better ventilated); Oct 2023 has a slight positive anomaly in south-central Delhi.

## Slide 38
India-ASI Stagnation Anomaly — November
November — peak stubble-burning month. Inversions jump to 30%, driving 8+ stagnant days on average. Nov 2021 shows a strong positive anomaly (+6–8 days above normal) — extreme inversion trapping. Nov 2022 also positive. Nov 2023–24 show negative anomalies, indicating better-than-average ventilation.

## Slide 39
India-ASI Stagnation Anomaly — December
December is peak stagnation: ~15 days/month. Dec 2022 shows a strong positive anomaly (more stagnant than avg), contrasting with the wind-only analysis where Dec 2022 was the most ventilated month. This reversal shows the India-ASI captures inversion-driven trapping that wind speed alone misses. Dec 2023 shows negative anomaly in SE Delhi.

## Slide 40
India-ASI Stagnation Anomaly — January
January climatology drops to ~8.5 days due to Western Disturbance rainfall (only 54.8% dry days). Jan 2024 shows a strong positive anomaly in western Delhi (+8–11 days) but negative in east — sharp spatial dipole suggesting localized inversion patterns. Jan 2021–22 both negative (well ventilated).

## Slide 41
India-ASI Stagnation Anomaly — February
February marks the winter-to-pre-monsoon transition. Inversions weaken (33.2%). Feb 2021 strongly positive in NW Delhi (+3 days); Feb 2023 is the standout with domain-wide positive anomaly (+6–8 days), indicating persistent late-winter stagnation. Feb 2022 and 2024 are negative (better ventilated).

## Slide 42
Validation of India-ASI using CPCB PM₂.₅
Step 2: Independent calibration against observed pollution
Methodology
• Stagnant days = India-ASI TRUE
• Non-stagnant days = India-ASI FALSE
• Compared network-average daily PM₂.₅ (26 stations, Oct–Feb, 2021–2024)
Key Result
• Stagnant: 259 µg/m³
• Non-stagnant: 211 µg/m³
• Difference: +48.7 µg/m³ (~23% higher)
Interpretation
• PM₂.₅ shifts upward on stagnant days
• Distribution becomes wider with more extremes
• Strong signal of pollutant trapping under weak dispersion
Box plot summary
Non-Stagnant
Stagnant
Mean: 211
Mean: 259
t-test: p = 2.25 × 10⁻⁸
The difference in mean PM₂.₅ is highly significant, not random.
What the t-test answers:
“Could this PM₂.₅ gap happen by chance?”
Conclusion: India-ASI stagnant days consistently correspond to higher CPCB PM₂.₅.

## Slide 43
Month-by-Month Interpretation of the Stagnant vs Non-Stagnant PM₂.₅ Plot
The important point is not only that stagnation matters, but that it matters differently in each month.
What each month tells us
The bars compare average PM₂.₅ on stagnant and non-stagnant days. The gap between the bars tells us whether meteorological trapping is stronger than the emission signal in that month.
October
~+2%: almost no difference. Stagnation has little power because the transition from monsoon to winter has just begun, so very few stagnant days exist.
November
−7%: the unusual month. Pollution is dominated by stubble-burning emissions, so even non-stagnant days remain very polluted. This is why the red bar is not higher here.
December
+19%: the stagnation signal becomes clear. Calm winds, weaker mixing, and dry conditions begin to trap pollutants and push the red bar above the blue bar.
January
+30%: the strongest effect. Winter inversions and shallow boundary layers are most intense, so stagnant days accumulate much more PM₂.₅ than non-stagnant days.
February
+10%: a weaker but still visible effect. Winter is relaxing, ventilation slowly improves, and the stagnation penalty remains moderate rather than extreme.
Conclusion: stagnation is a strong PM₂.₅ amplifier in December–January, while November is controlled mainly by emissions rather than dispersion.